From the Mountains to the Estuary:

From the Schoolyard to the Bay

Meaningful Watershed Experiences 
for Grade 6 Students

Created by:

With grant support from

The NOAA Bay Watershed Education Training (B-WET) Program

In partnership with:

Occoquan Bay National Wildlife Refuge

Manassas Battlefield National Park

Introduction to Vernier Probeware to discover:

”The State of Our Schoolyard”

Using the Vernier LabQuest and sensors

FOR PRACTICE getting started:

To Collect Data

- Ensure stylus is securely connected

- To power on LabQuest, press the silver button at the top left

- Connect the temperature sensor to one of the 4 available ports at the top (CH1, CH2, CH3, CH4) –  (these will be the ports we use for the other sensors – Turbidity, Dissolved Oxygen, pH, & Conductivity)

- Notice the temperature display on the screen

- Press the Collect button 		just below the screen. Data collection will begin, and a graph will show your data being plotted in real time.

- Notice that the screen changed to a graph and is collecting data over time (lower right corner)

- Press the Collect button 		again to stop data collection.

To Analyze the Data you collected

- After data collection (above), use the stylus to tap a point on your graph

- Notice (1) the lines to the x and y axes; (2) the circle around the point you chose, and (3) the readings at the right of your graph – these are the x and y readings for the point you chose

- You can make adjustments to the cursor location by using the left and right cursor keys on the keypad below the screen. Notice how the circle and lines move and the numbers at the right side change – these are the new points you are moving to.

To Collect Additional Data

- To start a second data collection run, tap the file         cabinet in the upper right corner. You should now see Run 2 displayed with a blank graph.

- Press the Collect button 		just below the screen. Data collection will begin, and a graph will show your data being plotted in real time.

- Press the Collect button 		again to stop data collection.

Saving your Data

- To save your data, tap File with the stylus

- In the drop down menu, tap Save

- The screen will change to a file list and allow you to type your filename (you will see untitled in the Name bar)

- Using the stylus, tap in the Name bar

- A keyboard will appear 	( ( (

- Using the back arrow, 	delete untitled and type the name of your file (“Rob’s Temp Data”)

To Turn OFF LabQuest, hold down Power          button for 3 seconds

Using the Vernier LabQuest with the Temperature Sensor

- To power on LabQuest, press the silver button at the top left

- Connect the temperature sensor to one of the 4 available ports at the top (CH1, CH2, CH3, CH4)

- Notice the temperature display on the screen

- Put stainless steel portion of temperature sensor into water you want to measure

  - Do not completely submerge the temperature sensor, the plastic part is not waterproof

- Press the Collect button 	              just below the screen. Data collection will begin, and a graph will show your data being plotted in real time.

- Notice that the screen changed to a graph and is collecting data over time (lower right corner)

- Press the Collect button 	           again to stop data collection.

- Refer to SAVING, VIEWING, & UPLOADING YOUR DATA to save, review, & upload your data.

- When you are finished with the temperature sensor:

  - Carefully unplug it from the LabQuest port and return it to its plastic storage bag.

Using the Vernier LabQuest with the pH Sensor

- Before you turn on LabQuest, remove the storage bottle from the pH sensor by unscrewing the lid, removing the bottle, and sliding the lid off of the blue sensor.

- With distilled water, thoroughly rinse the lower (blue) section of the sensor, especially the bulb.

  - Do not completely submerge the pH sensor, the handle is not waterproof

- To power on LabQuest, press the silver button at the top left

- Connect the pH sensor to one of the 4 available ports at the top (CH1, CH2, CH3, CH4)

  - Notice the pH display on the screen

- Put the blue portion of the pH sensor into the solution you want to measure

  - Do not completely submerge the sensor, the handle is not waterproof

- Press the Collect button 	               just below the screen. Data collection will begin, and a graph will show your data being plotted in real time.

- Notice that the screen changed to a graph and is collecting data over time (lower right corner)

- Press the Collect button 	             again to stop data collection.

- Refer to SAVING, VIEWING, & UPLOADING YOUR DATA to save, review, & upload your data.

- When you are finished with the pH sensor:

  - Carefully unplug it from the LabQuest port

  - Rinse the blue sensor with distilled water.

  - Slide the bottle lid onto the sensor (blue portion). Put the sensor into the storage bottle just until the bottom is submerged in the storage solution.

    - Do not store the sensor in distilled water. It should ONLY be stored in the storage bottle with a special solution

  - Screw the lid onto the storage bottle.

  - Return the sensor and storage bottle to the equipment box.

Using the Vernier LabQuest with the Dissolved Oxygen (DO) Sensor

- Before you turn on LabQuest, remove the blue protective cap from the tip of the probe and discard - DO NOT replace protective cap after 1st use

- Unscrew the membrane cap from the tip of the sensor.

- Using a pipet, fill the membrane cap with 1 mL of DO Electrode Filling Solution.

- Carefully thread the membrane cap back onto the sensor.

- Place the sensor into a container filled with about 100 mL of distilled water.

  - DO NOT completely submerge the DO sensor, the handle is not waterproof

- You must warm-up the Dissolved Oxygen for 10 minutes before using it

- Leaving the sensor in the water, power on LabQuest, (press the silver button at the top left)

- Connect the Dissolved Oxygen sensor to one of the 4 available ports at the top (CH1, CH2,…)

  - Notice the DO display on the screen (mg/L)

  - Do not use the dissolved oxygen sensor at the same time (in the same solution) as any other sensor (it is best to use the dissolved oxygen sensor by itself)

- Leave the sensor in the water and connected to LabQuest interface with the data collection program running for 10 minutes. The sensor must stay connected at all times to keep it warmed up. If disconnected for a few minutes, it will be necessary to warm up the probe again.

- After 10 minutes, you are now ready to collect data.

- Place the sensor into the water being tested (submerge 4–6 cm, less than the length of your index finger). DO NOT completely submerge the DO sensor, the handle is not waterproof

- Gently stir the sensor in the water sample.  To get accurate readings, there must always be water flowing past the probe tip when you are taking measurements.

  - IF the sensor is left still in calm water, the DO readings will be inaccurate (and appear to be dropping)

- Press the Collect button 	             just below the screen. Data collection will begin, and a graph will show your data being plotted in real time.

- Notice that the screen changed to a graph and is collecting data over time (lower right corner)

- Press the Collect button 	               again to stop data collection.

- Refer to SAVING, VIEWING, & UPLOADING YOUR DATA to save, review, & upload your data.

- When you are finished with the DO sensor:

- Carefully unplug it from the LabQuest port

- Rinse the sensor with distilled water.

- Slide the bottle lid onto the sensor. Put the sensor into the storage bottle ½ filled with distilled water. Ensure the sensor tip (membrane) is submerged in the distilled water.

- Screw the lid onto the storage bottle.

- Return the sensor and storage bottle to the equipment box.

Using the Vernier LabQuest with the Turbidity Sensor

- To power on LabQuest, press the silver button at the top left

- Ask your teacher if the sensor is already calibrated.  If it’s not, STOP - ask for help to calibrate it – go to CALIBRATING TURBIDITY SENSOR before continuing (it should be calibrated before use) (see back of this page)

- Connect the Turbidity sensor to one of the 4 available ports at the top (CH1, CH2,…)

  - Notice the Turbidity display on the screen (NTU)

- Put the water sample into the empty bottle (cuvette) – fill it to the top of the line (the meniscus should be at the top of the line for every measurement)

- Screw the lid on the bottle

- Turn it upside down four (4) times to mix anything that settled to the bottom (DO NOT SHAKE – shaking will produce air bubbles that will affect turbidity reading)

- Wipe the outside with a lint-free cloth or tissue

- Holding by the lid, insert into the Turbidity Sensor - **align the mark on the bottle (black triangle) with the mark on the sensor (white triangle) - **these marks must be aligned whenever a reading is taken

- Monitor the turbidity value on LabQuest - because particles will settle, turbidity readings should be taken soon after bottle is placed in the sensor

- Press the Collect button 	      just below the screen. Data collection will begin, and a graph will show your data being plotted in real time.

- Notice that the screen changed to a graph and is collecting data over time (lower right corner)

- Press the Collect button 	             again to stop data collection.

- Refer to SAVING, VIEWING, & UPLOADING YOUR DATA to save, review, & upload your data.

- When you are finished with the Turbidity sensor:

  - Carefully unplug it from the LabQuest port

  - Rinse the sample bottle (cuvette) with distilled water.

  - Screw the lid back on, and return the sensor and bottle to the equipment box.

CALIBRATING TURBIDITY SENSOR

- To CALIBRATE sensor before using (should be calibrated before 1st use)

- Connect the Turbidity sensor to one of the 4 available ports at the top (CH1, CH2,…)

- Notice the Turbidity display on the screen (NTU)

- Get the bottle (cuvette) containing the Turbidity Standard (STABLCAL FORMAZIN STANDARD)

- Turn it upside down four (4) times to mix anything that settled to the bottom (DO NOT SHAKE – shaking will produce air bubbles that will affect turbidity reading)

- Enter Calibration routine of LabQuest – with sensor connected, tap Sensors, then Calibrate, and choose Turbidity

- Holding the standard bottle (cuvette) by the lid, insert into turbidity sensor - **align the mark on the bottle (black triangle) with the mark on the sensor (white triangle) - **these marks must be aligned whenever a reading is taken

- Close the lid

- On the LabQuest, enter 100 in the NTU block in the top left

- Remove the bottle from the Turbidity Sensor

- For the 2nd Calibration point, fill the empty bottle (cuvette) with distilled water

- The meniscus should be at the top of the line for every measurement

- Screw the lid on the bottle

- Wipe the outside with a lint-free cloth or tissue

- Holding by the lid, insert into the Turbidity Sensor

- On the LabQuest, enter 0 (zero) in the NTU block in the top left

- You are now ready to collect turbidity data

Using the Vernier LabQuest with the Conductivity Sensor

- To power on LabQuest, press the silver button at the top left

- Connect the conductivity sensor to one of the 4 available ports at the top (CH1, CH2,…)

  - Notice the conductivity (µS/cm) display on the screen

- Using distilled water, rinse the end of the sensor

- Insert the sensor into the sample to be tested – be sure the opening is completely submerged

  - Do not completely submerge the conductivity sensor, the handle is not waterproof

- Be sure the Range switch is set to _____

- Gently stir the sensor in the water sample

- Wait for the reading on LabQuest to stabilize – this should take less than 10 seconds

- Press the Collect button 	      just     below the screen. Data collection will begin, and a graph will show your data being plotted in real time.

  - Notice that the screen changed to a graph and is collecting data over time (lower right corner)

- Press the Collect button 	               again to stop data collection.

- Refer to SAVING, VIEWING, & UPLOADING YOUR DATA to save, review, & upload your data.

- When you are finished with the Conductivity sensor:

  - Carefully unplug it from the LabQuest port

  - Rinse the conductivity sensor with distilled water

  - Blot it dry using a paper towel or lab wipe and return it to its storage box.

SAVING, VIEWING, & UPLOADING YOUR DATA

Saving your data

- To save your data, tap File with the stylus

- In the drop down menu, tap Save

- Tap the stylus in the Name bar where you see untitled

- Using the stylus with the keyboard use the back arrow to delete untitled and type the name of your file, then tap Save.

- IF you are adding data to an existing file, tap that filename and then tap Overwrite – this will add your new data set to the file.

Viewing your data

- You can view all data in one file on one graph.

- Using the stylus, tap Run 1 (or Run __) in the upper right corner.

- You will get a drop down menu with a list of your data runs (Run 1, Run 2, Run 3,….) and All Runs.

- Using the stylus, Either tap the data run you want to view or tap All Runs to view all data on one graph

Uploading your data to a computer

- On LabQuest open the file you want to transfer

  - Power on LabQuest, press the silver button at the top left

  - With the stylus, tap (select) File and tap (select) Open

  - Tap (select) the file you want to open, then tap (select) Open

- On your computer, open Logger Lite

- Connect the LabQuest USB cable to your computer, then to LabQuest

- You should see a pop-up window that indicates: Remote Data Available – Remote data have been detected. Would you like to retrieve the data now?

- Select Yes

- Select Retrieve remote data into the current file select Ok

- On your computer, Save your file (select File, then Save As, then name your file and select Save)

- You can now manipulate your data on your computer

# Text boxes

Data Collection and Analysis